## Slide 1
G28
Notes: TIME LIMIT IS 2MINS 30 SECONDS :D

## Slide 2: EEG-Maze: Controlling a 2D Maze game using a P300-based BCI
Apurva Singh, Ashka Shah Jaspreet Dodd, and Sahana Radha
G28
Notes: TIME LIMIT IS 2MINS 30 SECONDS :D

## Slide 3: Bridging thought and action…
Situation
What if you could navigate a 2D maze using nothing but a top-down view?
g.tec Unicorn Hybrid + Customized P300 Speller:
  A hands-free gaming experience!
Motivation
Demonstrate how brains signals can be converted into intuitive commands.
Explore P300 as a tool for control mechanism in BCIs.
G28
Maze Game 1
Testing signal quality!
Notes: Our team set out to build a real-time Brain-Computer Interface (BCI) game that allows users to navigate a 2D maze using EEG signals alone — no keyboard or controller input.
We used the g.tec Unicorn Hybrid EEG headset and its built-in P300 speller module to train a classifier that detects visual attention toward flashing directional cues (↑, ↓, ←, →). These classifier outputs were then used to control the maze player.
The motivation behind our project was to… (read the slide. lol)

## Slide 4: Bringing our tools together…
Core Idea
Use P300 event-related potentials to control user’s movement.
Train classifier on the four arrow keys using salient stimuli to evoke strong P300 signals.
G28
Training the classifier
Unicorn Hybrid Headset
Unicorn Suite
Filter and P300 classifier
UDP/LSL stream
Classifier output sent to PyGame
PyGame
On-screen movement
Notes: Our solution transforms attention into action by coupling the P300 speller’s classifier output with a real-time 2D maze game.
Read the core IDEA/SOLUTION to the presented SITUATION in the slide before. Then walk them through the steps of creating the BCI-gaming application:
> Signal acquisition via Unicorn Hybrid EEG headset
> Signal processing and classifier training via P300 speller module in Unicorn Suite.
> Sending classifier-output data via UDP/LSL to PyGame and creating a responsive interface.
> Game control!

## Slide 5: Getting things right… takes time!
Pipeline development
Setup and Calibration 😵
OSCAR artifact removal saved us hours!
(2) Maximizing the P300 signal 📈 as per the literature →
Salient visual cues (insects, reptiles, spooky)
Tuning stimulus timing (ISI =0.75s, Flash = 0.2s)
P300a vs. P300b (target vs. non-target discrimination)
(3) Signal integration and parsing
Created script to parse LSL output and reduce processing time
(4) Debugged data latency
Dual-monitor vs. single-monitor comparison for response latency
G28
Fear increases P300 response!
Notes: “We built, trained, and integrated a functional EEG-to-game control pipeline from scratch — debugging every link from classifier training to real-time signal parsing under hackathon time pressure.”
If wanted, explain
ISI = Inter-stimulus interval
Flash duration = 200ms

## Slide 6: Drum Roll…?
What we celebrated:
G28
What we can improve on:
3-directional control
18 correct classifications in a row!
Sub-300 ms latency
Demo of functional P300-based Maze
4th direction (UP) key registered in classifier but not transferred to game via UDP.
Improve classifier accuracy and reduce #flickers for game-input for faster gameplay!
More spooky/scary visuals! :D
Notes: Despite limited time and hardware hiccups, our prototype achieved stable real-time control in three directions — showing that even a small team can build a working closed-loop BCI game pipeline within a single hackathon.

## Slide 7: Looking back at our efforts
Some of the things we learned from this experience…
About BCIs…
> EEG-game integration is highly sensitive to latency
> Classifier performance depends not just on the model, but also the UI design!
> Modular design and interfacing across serves is key for efficiency
And not just only about BCIs..
> Ambition with Realism lets us create a Minimally Viable Prototype (MVP) that serves as a foundation for next-steps
> Celebrating every little win makes its easier to deal with the hiccups!
G28
Notes: The biggest lesson wasn’t about EEG or code — it was about systems thinking: how every layer, from neural signal to network packet, needs to talk to each other in real time.

## Slide 8: Fun times at QueensU!
G28
Special thanks to:
Dr. Susan Boehnke
Dr. Ethan Heming
TA Matthew Jacobs

## Slide 9: EEG-Maze: Controlling a 2D Maze game using a P300-based BCI
Apurva Singh, Ashka Shah, Jaspreet Dodd, and Sahana Radha
G28